SECTION 07460

SIDING - RusticSeries

** NOTE TO SPECIFIER ** Woodtone; siding.
This section is based on the products of Woodtone, which is located at:
8007 Aitken Rd.
Chilliwack, BC, Canada V2R 4H5.
Toll Free Tel: (800) 663-9844.
Fax: (604) 792-3976.
Web: http://www.woodtone.com.
Email: info@woodtone.com.
.
At Woodtone, we provide innovative finishing solutions that increase curb appeal and dependability, effectively filling the product and service gaps in the exterior finishing industry. Woodtone has been supplying high-quality custom coating for builders for over 35 years - we pride ourselves on being the leader in factory coating technology--delivering a consistent quality product every day. From our 3 facilities in the Pacific Northwest and British Columbia, our factories run year-round and can keep your production of finished homes rolling in any season.

Our wide range of product and service offerings allows all of our partners the ability to earn more on their projects by choosing the specific Woodtone products and services that suit your needs. We are here to support you through our range of products and services with the expectation of expanding our collective business and winning more projects, improved margins and exceptional, long-term customer satisfaction. Our vision is to grow and develop our capabilities, our offerings, our systems and our people. We will build sustainability into everything we do, so that the next generation will be as proud of this business as we are.

- GENERAL

  - SECTION INCLUDES

    - Siding of the following types:

** NOTE TO SPECIFIER ** Delete items below not required for project.

      - Engineered Wood Horizontal Siding (RusticSeries).

      - Engineered Wood Vertical Siding (RusticSeries).

      - Engineered Wood Shake Panels (RusticSeries).

      - Fiber Cement Horizontal Siding (RusticSeries).

      - Fiber Cement Vertical Siding (RusticSeries).

      - Fiber Cement Shake Panels (RusticSeries).

  - RELATED SECTIONS

** NOTE TO SPECIFIER ** Delete any sections below not relevant to this project; add others as required.

    - Section 06201 - Exterior Finish Carpentry.

    - Section 06620 - Wood, Fiber Cement and Composite Trim.

    - Section 07400 - Siding Panels.

    - Section 09900 - Painting.

  - SUBMITTALS

    - Submit under provisions of Section 01300.

    - Product Data: For each type of process and factory-fabricated product. Indicate component materials, dimensions, profiles, textures, and colors and include construction and application details.

      - Preparation instructions and recommendations.

      - Storage and handling requirements and recommendations.

      - Installation methods.

** NOTE TO SPECIFIER ** Delete if not required for project.

    - Research/Evaluation Reports: For fire-retardant-coated wood.

    - Verification Samples: For each finish product specified, two samples, representing actual product and color.

  - QUALITY ASSURANCE

** NOTE TO SPECIFIER ** Delete if not required for project.

    - Installer Qualifications: Installer shall be licensed, registered or otherwise acceptable to authorities having jurisdiction to install exterior building products.

  - DELIVERY, STORAGE, AND HANDLING

    - Inspect the materials upon delivery to assure specified products have been received. Store products in a safe area, away from construction traffic. Store under cover and off the ground, protected from moisture. Follow Care and Maintenance Guide by Woodtone.

  - PROJECT CONDITIONS

    - Maintain environmental conditions (temperature, humidity, and ventilation) within limits recommended by manufacturer for optimum results. Do not install products under environmental conditions outside manufacturer's recommended limits.

  - WARRANTY

** NOTE TO SPECIFIER ** Delete warranty types not required.

    - Material Warranty: Provide manufacturer's standard warranty and as follows:

** NOTE TO SPECIFIER ** Delete material warranty not required.

      - RusticSeries: As provided by siding substrate manufacturer.

    - Coating Warranty: Provide manufacturer's standard warranty and as follows:

** NOTE TO SPECIFIER ** Delete coating warranty not required.

      - RusticSeries Coatings: 20-year warranty on the coating when factory applied.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: Woodtone, which is located at: 8007 Aitken Rd.; Chilliwack, BC; Canada V2R 4H5; Toll Free Tel: 800-663-9844; Fax: 604-792-3976; Email: request info (info@woodtone.com); Web: www.woodtone.com

** NOTE TO SPECIFIER ** Delete one of the following two paragraphs; coordinate with requirements of Division 1 section on product options and substitutions.

    - Substitutions: Not permitted.

    - Requests for substitutions will be considered in accordance with provisions of Section 01600.

  - SIDING

** NOTE TO SPECIFIER ** Delete if not required for project.

** NOTE TO SPECIFIER ** Delete if not required for project.

    - Substrate: Engineered Wood Siding; LP building products, factory coated by Woodtone.

** NOTE TO SPECIFIER ** Delete type not required for project.

      - Type: Horizontal Wood Fiber Composite Siding: LP SmartSide as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Lap siding, 5-7/8 inches (149 mm) wide.

        - Style: Lap siding, 7-7/8 inches (200 mm) wide. .

        - Style: Lap siding, 11-7/8 inches (301 mm) wide.

        - Style: ___________.

        - Style: As per sample.

        - Style: As indicated on Drawings.

** NOTE TO SPECIFIER ** Delete thickness not required.

        - Thickness: 3/8 inch.

        - Thickness: 7/16 inch.

        - Texture: Cedar.

        - Length: 16 feet (4876 mm).

      - Type: Vertical Wood Fiber Composite Siding: LP SmartSide as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Panel siding; Reverse Board and Batten.

        - Style: ___________.

        - Style: As per sample.

        - Style: As indicated on Drawings. .

** NOTE TO SPECIFIER ** Delete thickness not required.

        - Thickness: 3/8 inch.

        - Thickness: 7/16 inch.

        - Thickness: 19/32 inch.

        - Texture: Cedar.

        - Length: Single lengths as applicable.

      - Type: Shake Panel Wood Fiber Composite Siding: LP Cedar Shake as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete pattern not required.

        - Style: Shake siding; 12 inch wide.

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

        - Thickness: 7/16 inch.

        - Texture: Cedar.

        - Length: 48 inch.

      - Finish: Factory coating by Woodtone.

** NOTE TO SPECIFIER ** Delete procedure not required for project.

** NOTE TO SPECIFIER ** Delete color not required for project.

        - Color: RusticSeries Summer Wheat.

        - Color: RusticSeries Old Cherry.

        - Color: RusticSeries River Rock.

        - Color: RusticSeries Rosewood.

        - Color: RusticSeries Aspen Ridge.

        - Color: RusticSeries Smokey Alder.

        - Color: RusticSeries Coastal Gray.

        - Color: RusticSeries Mountain Cedar.

        - Color: RusticSeries Vintage Cabernet.

        - Color: RusticSeries Tamarack Green.

        - Color: RusticSeries Roasted Walnut.

        - Color: RusticSeries White Granite.

        - Color: RusticSeries Warm Espresso.

        - Color: RusticSeries Cascade Slate.

        - Color: RusticSeries Winchester Brown.

        - Color: RusticSeries Stone Blue.

        - Color: RusticSeries Wild Berry.

        - Color: RusticSeries Timber Trail.

        - Color: ________.

        - Color: As per sample.

        - Color: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete if not required for project.

    - Substrate: Fiber Cement Siding; Allura products as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete type not required for project.

      - Type: Horizontal Fiber Cement Siding: WeatherBoards as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Lap siding; 5-1/4 inches (133 mm) wide.

        - Style: Lap siding; 6-1/4 inches (159 mm) wide. .

        - Style: Lap siding; 7-1/4 inches (185 mm) wide. .

        - Style: Lap siding; 8-1/4 inches (210 mm) wide. .

        - Style: Lap siding; 9-1/4 inches (235 mm) wide. .

        - Style: Lap siding; 12 inches (305 mm) wide. .

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete texture not required.

        - Texture: Traditional

        - Thickness: 5/16 inch (7.9 mm).

        - Length: 12 feet (3657 mm).

      - Type: Vertical Fiber Cement Siding: WeatherBoards as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Traditional, no groove Panel; 4 feet wide.

        - Style: Traditional, groove Panel; 4 feet wide.

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete style not required.

        - Length: 8 feet.

        - Length: 9 feet.

        - Length: 10 feet.

      - Type: Shake Panel Fiber Cement Siding: WeatherBoards as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete Style not required.

        - Style: Perfection Shingles; 8-1/4 inch wide by 12 feet long.

        - Style: Random Square Straight Edge, 12 inch wide by 4 feet long.

        - Style: Random Square Straight Edge, 16 inch wide by 4 feet long.

        - Style: Random Square Staggered Edge; 16 inch wide by 4 feet long.

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

      - Finish: Factory Finish Top Coating by Woodtone.

** NOTE TO SPECIFIER ** Delete procedure not required for project.

** NOTE TO SPECIFIER ** Delete color not required for project.

        - Color: RusticSeries Summer Wheat.

        - Color: RusticSeries Summer Wheat.

        - Color: RusticSeries Old Cherry.

        - Color: RusticSeries River Rock.

        - Color: RusticSeries Rosewood.

        - Color: RusticSeries Aspen Ridge.

        - Color: RusticSeries Smokey Alder.

        - Color: RusticSeries Coastal Gray.

        - Color: RusticSeries Mountain Cedar.

        - Color: RusticSeries Vintage Cabernet.

        - Color: RusticSeries Tamarack Green.

        - Color: RusticSeries Roasted Walnut.

        - Color: RusticSeries White Granite.

        - Color: RusticSeries Warm Espresso.

        - Color: RusticSeries Cascade Slate.

        - Color: RusticSeries Winchester Brown.

        - Color: RusticSeries Stone Blue.

        - Color: RusticSeries Wild Berry.

        - Color: RusticSeries Timber Trail.

        - Color: ________.

        - Color: As per sample.

        - Color: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete if not required for project.

    - Substrate: Fiber Cement Siding; James Hardie products as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete type not required for project.

      - Type: Horizontal Fiber Cement Siding: HardiePlank as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Lap siding; 5-1/4 inches (133 mm wide).

        - Style: Lap siding; 6-1/4 inches (159 mm) wide. .

        - Style: Lap siding; 7-1/4 inches (185 mm) wide. .

        - Style: Lap siding; 8-1/4 inches (210 mm) wide. .

        - Style: Lap siding; 9-1/4 inches (235 mm) wide. .

        - Style: Lap siding; 12 inches (305 mm) wide. .

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete texture not required.

        - Texture: Smooth with eased edge.

        - Texture: Smooth with squared edge.

        - Texture: Cedarmill with eased edge.

        - Texture: Cedarmill with squared edge.

        - Texture: ___________.

        - Texture: As per sample.

        - Texture: As indicated on drawings.

        - Thickness: 5/16 inch (7.9 mm).

        - Length: 12 feet (3657 mm).

      - Type: Vertical Fiber Cement Siding: HardiePanel as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete style not required.

        - Style: Stucco Panel; 4 feet wide.

        - Style: Smooth Panel; 4 feet wide.

        - Style: Cedarmill Panel; 4 feet wide.

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete style not required.

        - Length: 8 feet.

        - Length: 9 feet.

        - Length: 10 feet.

      - Type: Shake Panel Fiber Cement Siding: HardieShingle as coated by Woodtone.

** NOTE TO SPECIFIER ** Delete Style not required.

        - Style: Heritage Straight Edge; 15.25 inch wide.

        - Style: Heritage Staggered Edge; 15.25 inch wide.

        - Style: Heritage Half-Rounds; 15.25 inch wide.

        - Style: __________.

        - Style: As per sample.

        - Style: As indicated on drawings.

        - Length: 8 feet.

      - Finish: Factory Finish Top Coating.

** NOTE TO SPECIFIER ** Delete procedure not required for project.

** NOTE TO SPECIFIER ** Delete color not required for project.

        - Color: RusticSeries Summer Wheat.

        - Color: RusticSeries Old Cherry.

        - Color: RusticSeries River Rock.

        - Color: RusticSeries Rosewood.

        - Color: RusticSeries Aspen Ridge.

        - Color: RusticSeries Smokey Alder.

        - Color: RusticSeries Coastal Gray.

        - Color: RusticSeries Mountain Cedar.

        - Color: RusticSeries Vintage Cabernet.

        - Color: RusticSeries Tamarack Green.

        - Color: RusticSeries Roasted Walnut.

        - Color: RusticSeries White Granite.

        - Color: RusticSeries Warm Espresso.

        - Color: RusticSeries Cascade Slate.

        - Color: RusticSeries Winchester Brown.

        - Color: RusticSeries Stone Blue.

        - Color: RusticSeries Wild Berry.

        - Color: RusticSeries Timber Trail.

        - Color: ________.

        - Color: As per sample.

        - Color: As indicated on drawings.

** NOTE TO SPECIFIER ** Delete if not required for project.

  - FINISH COATING SYSTEM

** NOTE TO SPECIFIER ** Every order coated by Woodtone is done within a factory controlled environment, where we machine coat and even hand brush your project to achieve the look and finish that you want. Our commitment to quality goes beyond our factory--Our methods are approved by all the major paint manufacturers and as an Authorized Factory Applicator of their paint products, we are able to offer extended coating warranties that range up to 30 years on practically any paint or stain. With thousands of different paints available in the market Woodtone will continue to endeavor to select paint partners who produce products which offer both superior performance and environmental benefits.

    - Wood Appearance Proprietary Two Coat System.

  - FASTENERS

    - Nails for Fiber Cement Siding and Engineered Wood Siding with Woodtone RusticSeries Coating: As recommended by fiber cement siding manufacturer.

- EXECUTION

  - PREPARATION

    - Clean surfaces thoroughly prior to installation.

    - Prepare surfaces using the methods recommended by the manufacturer for achieving the best result for the substrate under the project conditions.

  - INSTALLATION

    - Install in accordance with manufacturer's instructions including the following:

      - Coordinate work with related trades; scribe and cope siding boards for accurate fit. Allow for installation of related work to avoid cutting and patching.

      - Select siding boards of longest practical lengths. Discard boards that are warped, twisted, bowed, crooked or otherwise defective.

      - Comply with siding manufacturer's and substrate manufacturer's installation instructions. Comply with local building codes and regulations.

      - Apply touch up coating on surfaces and ends cut during installation.

      - As work proceeds, maintain premises free of unnecessary accumulation of tools, equipment, surplus materials, and debris related to this work.

    - Finish materials on all ends and sides and ends. Apply touch up coating on new cuts. Factory finishing is preferred.

  - PROTECTION

    - Protect installed products until completion of project.

    - Touch-up, repair or replace damaged products before Substantial Completion.

END OF SECTION